General:
The command parser is built to accept short strings of ascii data, compacted to reduce data transfer size while being easy to handle by standard UART hardware. The general form is a letter indicating which operation to perform followed by a series of numbers and letters, and finally a carriage return and line feed. As a string, an example command would be “M0F50\r\n”.

Return codes:

Overflow ("ovf"): The input buffer is filled (no command should be that long). Send delimiter to clear buffer
Invalid Syntax ("inv"): The first character in the command is not one of the defined prefixes.
Formatting Error ("fmt"): There was something generally wrong with the command, like it had the wrong number of characters or an out of range value was detected.
No Motor ("nom"): The motor's number is past the most downstream slave detected.

Drive motor:
Set a motor's drive level in percent.
"Mndl"
n = motor number, single or double digits
d = direction, R or F
l = level, 0 to 100

Example:
"M1F34" – Drive master motor B forward at 34%.
"M2R80" – Drive slave motor A reverse at 80%.

Switch motor polarity:
"MnS"
n = motor number, single or double digits

Example:
"M1S" – Switch polarity of motor 1. F becomes R, and vicea-versa.

Write register:
"Wrrhh"
rr = two digit hex address
hh = two digit hex data

Example:
"W20FF" – Write 0xFF to register 0x20 (MA_DRIVE).

Read register:
"Rrr"
rr = two digit hex address

Example:
"R01" – Read address 0x01 (ID), bus will display "A9", ID word of 0xA9

UART Baud:
"Un"
n = baud rate selection

This command changes the bitrate of the UART. The serial terminal will need to be reconfigured after this command. The command reports new rate at old baud before changing to the new one.

Rates supported:
1 – 2400
2 – 4800
3 – 9600
4 – 14400
5 – 19200
6 – 38400
7 – 57600
8 – 115200

Examples:
"U3" – Set baud rate to 9600
"U8" – Set baud rate to 115200

Bridge/unbridge outputs:
"Brr"
rr = Motor driver number, 0 is master, 1-16 is slave

This causes a motor driver to start or stop synchronous PWM on both 'A' and 'B' ports. Sending again will un-bridge the driver. Notice that the input is by board number, not motor number.

Example:
"B0" – Bridge master's outputs
"B2" – Bridge the 2nd physical slave's outputs (motors 4&5)

Enable/disable outputs:
"E"

Example:
"E" – Enable all outputs
"E" (a second time) – Disable all outputs