# Buses
## Test the I2C user interface
This test checks all the ways a user can connect the I2C interface.

Procedure:
1. Test the following configurations:
  1. SCMD master at any lowest address, 100 kHz redboard Pass
  2. Two SCMD masters, one at highest address, 100 KHz redboard Pass
  3. 400 KHz on teensy (Low priority) Skipped
2. For each configuration, run the diag example and look for errors. Pass

Criteria:
Did the EUTs behave normally?? YES

## Test the SPI user interface
This test checks all the ways a user can connect the SPI interface.

Procedure:
1. Test the following configurations:
  1. SCMD master at 1 MHz Tested at 500kHz and 1 MHz, Pass
  2. Two SCMD masters with different CS pins. Pass
2. For each configuration, run the diag example and look for errors. Pass

Criteria:
Did the EUTs behave normally? YES

## Test the UART user interface
Procedure:
1. Test the following configurations:
  1. SCMD at default baud Pass
  2. SCMD at 57600 baud by jumper Pass
  3. SCMD at 115200 baud by jumper Pass
  4. Other configurations by using the commands U0-U7. Pass
2. Test that the number are accepted as 1 or two digit for most, and 3 for drive percent Pass
3. Test that enable is passed to slaves Pass
4. Test that E, B, and MxxS commands result in the proper bit flipped within INV_X_X, BRIDGE_SLV_X registers Pass
#define SCMD_INV_2_9 0x50
#define SCMD_INV_10_17 0x51
#define SCMD_INV_18_25 0x52
#define SCMD_INV_26_33 0x53
#define SCMD_BRIDGE_SLV_L 0x54
#define SCMD_BRIDGE_SLV_H 0x55
Criteria:
Did the EUTs behave normally?? YES
# FW elements
For these tests, connect 16 slaves and perform the following actions using the registerRWtool
## Test motor driving registers
Make sure motor information is passed to the correct locations

Procedure:
1. Test that the following motors drive when master locations are written: Pass
  1. motor 0,1, 2, 3, 4, 5, 17, 18, and 33

Criteria:
Do commands cause correct change on all motors? YES

## Test slave configuration
Test that writing to slave and global registers passes the information on to the slaves correctly. For these tests remote access is required by remote window or arduino function.
1. Motor 2, 9, 10, 17, 18, 25, 26 and 33 Pass
2. Bridge 0, 1, 8, 9, and 16 Pass
#define SCMD_MOTOR_A_INVERT 0x12
#define SCMD_MOTOR_B_INVERT 0x13
#define SCMD_BRIDGE 0x14

Procedure:
1. Write a pattern to INV regs and read remote local inversion regs. Pass
2. Write a pattern to BRIDGE regs and read remote local bridging regs Pass
3. Check that the following are passed directly (global config) to the associated local slave registers.
  1. DRIVER_ENABLE Pass
  2. MASTER_LOCK Pass
  3. USER_LOCK Pass
  4. FSAFE_TIME Pass

Criteria:
Are all values passed correctly? YES

## Check lock protections
Make sure the master and user locks operate

Procedure:
1. Write each "R" register with master key removed, then use REG_OOR_CNT to verify if they were protected Pass
2. Write each "user lock"able register with the user key removed, then use REG_OOR_CNT to verify they did not accept the data. Pass
3. Write each "user lock"able register with the user key inserted, REG_OOR_CNT should read 0. Pass
4. Write a new FID in with both keys inserted, and read back to verify. Pass

Criteria:
Were the locks capible of preventing or allowing the correct operations? YES

## Test the failsafe mode
This checks that all modes of failsafe operate

Procedure:
1. Probe config out and exp. data
2. Set the FSAFE_TIME(0x76) to 0xC8 for 2 second failsafe time Pass
3. Set FSAFE_CTRL:
  1. Use b1 for drive off/last behavior Pass
  2. Set 0x02 for reboot Pass
  3. Set 0x04 for re-enumerate. Pass
  4. Set 0x08 for user port re-init. Pass – works but doesn't recover data
  5. Set 0x10 for expansion port re-init Pass
4. Check the slave contents of FSAFE_TIME to determine if configuration was properly transfered during re-enumerate. Yes

Criteria:
Did the EUT recover as expected? Yes

## Test enumeration
Check that enumeration occurs correctly. For many of these, reading 0x0B for top address may be useful.

Procedure:
1. Check that enumeration occurs successfully for 0, 1, 2, and 16 slaves. Pass
2. Issue a reboot by CONTROL_1 for 16 Pass
3. Configure some global settings
4. Issue a re-enumeration by CONTROL_1 for 16 slaves
5. Check that global settings were correctly passed to slaves Pass
6. Configure master config in pin with MST_E_IN_FN and test function by shorting config_in to ground Pass

Criteria:
1. Does the top address match for various slaves? YES?
2. Do both reboots result in a proper enumeration? YES?
3. Do both reenumerations result in the correct configuration? YES?
## Test the expansion bus speed setting
Check that the expansion bus can be configured by inspecting with a scope.

Procedure:
1. Measure the bit rate of the defualt 100KHz setting
2. Configure and test the 50KHz and 400 KHz settings using E_BUS_SPEED
3. Measure the slave motor data packets dead time, and set UPDATE_RATE to change Pass
4. With UPDATE_RATE set to 0, does a packet occur after writing FORCE_UPDATE to 1? Pass

Criteria:
Are bus configuration parameters effecting operation properly? YES

## Test an item in the Test Plan
Describe the intent of the item to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO