# Functional Test Record
## 1) Test thermal performance of the board and DRV8835
Determine temperature rise of board operating at max drive

Procedure:
1. Attach resistors to output channels such that they consume 1.5A at 11.0V supply
2. Attach termocouple to DRV8835
3. Lay EUT flat on FR4 "burn surface", or something with marginal thermal conductivity. Allow top-side convection.
4. Target FliR cam at EUT
5. Starting with low drive,
  1. Set drive level
  2. Measure current at that drive level
  3. Wait for EUT to stabilize
  4. Record final temperature of DRV8835
  5. Take a thermal picture
  6. Increment drive level

Criteria:
Unknown – Does EUT satisfy typical use cases? YES/NO
## 2) Input Voltage Range
Check that the EUT operates normally under the full voltage range of the product, under various loads

Procedure:
1. Attach current and voltage meters to input
2. Power the EUT with variable supply
3. Attach voltage monitor to VREG pin
4. Build up 3 resistive loads, each for 1.5 A at input voltages of 3.0V 6.0V and 11V
5. Resistors selected:
  1. 3.0V range
  2. 6.0V range
  3. 11.0V range
6. Operate the drive on both channels while measuring the VREG pin, input current, and input voltage. Create a graph

Criteria:
1. Does the EUT function as expected? YES/NO
2. Is the output voltage liner to drive at all levels? YES/NO

## 3) Test Current Resistance in board
Determine if the PCB is limiting current to the board

Procedure:
1. Measure input voltage and current, apply 11.0V
2. Attach 11.0 V resistors to output terminals
3. Drive both outputs max each way.

Criteria:
Do both outputs deliver 1.5A? YES/NO
## 4) Test LDO power dissipation
Calculate the power dissipated by the LDO

Procedure:
1. Split the power out trace on the bottom of the board near the VREG pin, insert current meter
2. Measure voltage in, current in, voltage out(VREG), current out
3. Take measurements across voltage range in 1v increments
4. Produce a graph of the power consumed by the LDO

Criteria:
Is the power dissipated less than 1/4 watt? YES/NO

## 5) Determine resistance to back-EMF generated by manually pushed motors
Test that forcing the drive motors around during drive does not damage the EUT

Procedure:
1. Supply the EUT through a 0.5 to 1.0 ohm resistor, RECORD VALUE HERE
2. Attach a scope to VREG and VIN
3. Attach motors to output drives
4. Do the following for 3.0V, 6.0V, and 11.0V supply levels
  1. Increment the drive levels
  2. Spin and mess with the motors
  3. Record peaks levels from scope
5. Capture 1 or more

Criteria:
1. Do the levels stay within absolute maximums? YES/NO
2. Does the EUT continue to operate normally? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO