# index
Text

Serial Controlled Motor Driver Datasheet and Manual

# Features
Basic Features
- 127 levels of DC drive strength.
- Controllable by I2C, SPI, or TTL UART signals
- Stock 3.3v logic levels
- Direction inversion on a per motor basis
- Global Drive enable
- Expansion port utalizing I2C that allows 16 additional drivers
- Auto-enumeration of slaves based on connection of expansion 'In' and 'Out' connections.
- Exposed TO-220 heatsink shape
- 12 selectable I2C addresses

Advanced Features
- Bridging (between channels of a single board, to double current)
- VCC breakable to allow up to 5.5v levels.
- PSoC programming port included.
- Master can report bus diagnostics
- Configurable failsafe time and operation
- Configurable expansion bus bitrate to 50, 100, or 400 kHz.
- Configurable expansion bus update rate from 1ms to 255ms, or by command only.

Electrical and Thermal Specs
- 1.5 A peak drive per channel
- Operates from 3 to 11 volts with 12v absolute max
- Thermal limits
  - 500mA / channel -- T.case = 50 Deg C
  - 1A / channel -- T.case = 90 Deg C
  - 1.2A / channel -- T.case = 110 Deg C
  - 1.5A / channel -- forced air cooling or heatsink required
# Basic Ideas
Communication Perspective
A single driver board is capible of being expanded by adding one or more slaves. Illustration 1 shows a master connected to a slave, with the user controlling by microcontroller or computer.
Illustration 1: A basic topology

To avoid confusion, a few terms are defined here.
User Port – Connects the user’s project to the master SCMD and is unused on slaves.
Expansion Port – Connects a single master and up to 16 slaves, and should never be connected to the user’s project.
Master – The SCMD which is connected to the user’s project. Also, it is the I2C master on the expansion port
Slave – A SCMD which is only connected to a master scmd by way of the expansion port.
Note: The config in and out pins of the expansion port may sometimes be connected to the user’s project for error checking and mitigation purposes.

Motor Polarity – The driver and this document often omit motor polarity. This is because polarity to spin direction is not standardized, and it is assumed the user will attach them backwards 50% of the time. Each motor channel is independently configurable for what is thought of as ‘forward’ spin by command. It is assumed that the user will first attach the motors, then decide which channels need to be inverted and issue inversion settings at boot time.

Numbering – Each SCMD has two channels, A and B. When they are bridged the B channel becomes a duplicate A, and the drive is doubled.
Motors in a chain of several motor drivers are all referenced by motor number, starting from master's A channel as zero, B as 1, then the first slave's A channel as 2, and so on up to motor 33. When a driver board is bridged, it still has both motor numbers associated with it, however controlling what was the B channel will have no effect.

When performing bridging, driver board are numbered 0 to 16. The master is driver number 0, the first slave is driver 1, etc.
# Operational Description
Breif
The main elements of the motor driver are a microcontroller and dual H-bridge driver, with a voltage regulator for the logic end of things.

The SCMD has been designed to emulate a typical I2C or SPI perhipherial. Inside, there is a set of memory locations named registers. By writing into some registers, the SCMD takes action. Other registers have data that can be used, but writing does not cause action within the SCMD. Generally, the SCMD sits idle waiting for changes to registers, then performs actions based on new data.
During boot, the SCMD captures the contents of the config jumpers into a register and uses that value to determine which serial configuation to choose. They are set by entering a number from 0 to 15 in 4 bit binary, with a solder jumper indicating a '1'.
The SCMDs are equipted with an expansion I2C bus, wher they can be gained to form a group of motors that can all be controlled by talking to the master only.
For I2C busses, pull-up resistors are provided and default disabled. The slave bus requires a single set enabled for any number of slaves. If I2C is used, the user pull-up jumper must be closed, or pull-up resistors supplied externally.
The SCMD has been released with an Arduino library that performs high level functions by writing the correct registers, and can ease demonstration. The library also has functions to read or write the registers directly.
Register access aafeguards
Certain registers are designated "User unlockable". These registers contain configuration data for the current application. To provent accidental writes a user lock register exists. When the user lock contains the user key byte, the user lock registers can be written to. The default is unlocked.
Registers that are designated read-only are actually also writeable, to no documented end. A global lock exists to allow writes to these addresses. Note that the global lock is protected by the user lock, so both are needed to allow write access.
Slave operation
Multiple SCMDs can be connected to create a group of controllable motors. In this case, certain registers within the master cause changes to the slaves.
Writing to the drive registers in the master do not instanly update the drive levels. Instead, the master saves the new drive levels and sends them to the slaves on a periodic loop (configurable rate or by manual request). There are 34 registers that contain drive levels for each of the possible motor numbers. Writing to any of these registers in the master causes that motor in the slave chain to match the drive level after the next transmission.
Writing to the "Global setting" registers cause immediate action. The register contents will be applied locally and then sent out to the slaves.
H-Bridge driver control
The H-Bridge driver is essentially a dual, two leg totem pole drive with control logic. The default power-on state is to have the drives completely disabled with all 4 outputs at zero. Configuring the SCMD causes the driver to connect to two PWM generators, choosing polarity and source. They can be configured such that both outputs will be time and duty syncronized, allowing bridging of the output terminals for double current.
Power-on enumeration
When power is first applied, the master operates at the selected serial confiuration and address, and all slaves exist on an address that is not used. When the master is ready, it triggers the first driver to move to a polling address, and accept an assigned address from there. In turn, each slave receives an address in this manner.
When the master can't get a response within a set number of tries, enumeration stops and the master is ready to accept control.
Failsafe operation
The default operation of the SCMD is to simply drive the motors at the last level indicated until another command come in. To pervent run-away situations a Failsafe is implemented. When configured, the drivers will remove power to the outputs if the serial bus remains inactive for a period of time, which can be set up to 2.5 seconds.
The config in pin on the master and slaves can also work as a reset line. For the slaves, bringing the line low. resets the device. For the master, pulsing the line can cause either low-level reboot or re-enumeration of the slaves.
Using these two features, a system can be made to recover from many situations.
Status LED
There is a single LED on the motor driver, that blinks to indicate status, and blips to indicate serial port activity. A normally operating blinks once with much space inbetween while an error state will be displayed as a fast group of flashing. Reception of data will cause a slight blip in the LED. When a steady stream of data is being received, the LED will display dim with the other status message overlaid.
# Electrical properties
## Absolute maximum
## Electrical Characteristics
## Thermal
# Pin functions

Illustration 2: test
# Communication interfaces
## User port I2C
## User port SPI

## User Port UART and Command Set
General:
All commands delimited by \n.
If command length exceeds buffer, bus will return "ovf" (overflow). Send delimiter to clear buffer
If command not valid, bus will return "inv" (invalid syntax)
If command not formatted correctly, bus will return "fmt" (formatting error)
If command addresses motor on slave which is not present, bus will return "nom" (no motor)

Drive motor:
"Mndl"
n = motor number, single or double digits
d = direction, R or F
l = level, 0 to 100

Example:
"M1F34" – Drive master motor B forward at 34%.
"M2R80" – Drive slave motor A reverse at 80%.

Switch motor polarity:
"MnS"
n = motor number, single or double digits

Example:
"M1S" – Switch polarity of motor 1. F becomes R, and vicea-versa.

Write register:
"Wrrhh"
rr = two digit hex address
hh = two digit hex data

Example:
"W20FF" – Write 0xFF to register 0x20 (MA_DRIVE).

Read register:
"Rrr"
rr = two digit hex address

Example:
"R01" – Read address 0x01 (ID), bus will display "A9", ID word of 0xA9

UART Baud:
"Un"
n = baud rate selection

Rates supported:
1 – 2400
2 – 4800
3 – 9600
4 – 14400
5 – 19200
6 – 38400
7 – 57600
8 – 115200

Example:
"U3" – Set baud rate to 9600
"U8" – Set baud rate to 115200

Bridge/unbridge outputs:
"Brr"
rr = Motor driver number, 0 is master, 1-16 is slave

Example:
"B0" – Bridge master's outputs
"B2" – Bridge the 2nd physical slave's outputs (motors 4&5)

Enable/disable outputs:
"E"

Example:
"E" – Enable all outputs
"E" (a second time) – Disable all outputs
## Expansion port

# Arduino Library API Reference

# Control registers
## Memory map

## Descriptions
0x00: FID
Reports firmware version. This corrisponds with the numbering within the gitub repository.
https://github.com/sparkfun/Serial_Controlled_Motor_Driver/tree/RevisionRepaired/Firmware/Releases
0x01: ID
Reports hard-coded ID byte of 0xA9
0x02: SLAVE_ADDR
This register reflects the driver's address as a slave on the expansion bus only. Writing to it changes the address of the slave. This register is used by the master during slave enumeration.
0x03: CONFIG_BITS
Reflects jumper position on bottom of board, and controls how the firmware behaves on a fundemental level. This value should not be changed during operation.
0x04: U_I2C_RD_ERR
This reports number of times the PSoC's USER PORT serial device had a read error while in I2C slave mode.
Write 0x00 to clear.
0x05: U_I2C_WR_ERR
This reports number of times the PSoC's USER PORT serial device had a write error while in I2C master mode.
Write 0x00 to clear.
0x06: U_BUF_DUMPED
This reports the number of times the USER PORT's RX buffer abandoned with data still in it, while in I2C or SPI mode. This can happen if data comes in too fast or if unformed garbage data is received.
Write 0x00 to clear.
0x07: E_I2C_RD_ERR
This reports number of times the PSoC's EXPANSION PORT serial device had a read error while in I2C slave mode.
Write 0x00 to clear.
0x08: E_I2C_WR_ERR
This reports number of times the PSoC's EXPANSION PORT serial device had a write error while in I2C slave mode.
Write 0x00 to clear.
0x09: UPORT_TIME
This register contains the amount of time the USER PORT's slave ISR took. It contains a peak value that can be read as the longest time since the last clear.
Write 0x00 to clear.
0x0A: SLV_POLL_CNT
This register is used by the master to count the number of times it has polled for a slave. After enumeration is complete, this will read the max poll limit plus 1. (201)
0x0B: SLV_TOP_ADDR
This register reflects the address of the most down-stream slave, and is determined during slave enumeration. The master uses this value to determine how many slaves to broadcast to, and it is unused in the slaves. By comparing it with the #defined START_SLAVE_ADDR, the number of attached slaves can be determined by the user. Writing to this register will effect the depth of updates that occur, and should never need to be done.
If this register reads a value lower than START_SLAVE_ADDR, no slaves were detected.
0x0C: MST_E_ERR
Counts number of times a master had a general timeout on communication with the attached slaves.
Write 0x00 to clear.
0x0D: MST_E_STATUS
Reports the last error status response from writing a double value to the slaves.
0x0E: FSAFE_FAULTS
The failsafe ISR hit count. This is incremented every time the watchdog is not satisfied and the ISR is allowed to run.
Write 0x00 to clear.
0x0F: REG_OOR_CNT
This counts the number of times anybody tried to write outside of the range of available registers. This should always remain at 0.
Write 0x00 to clear.
0x10: REG_RO_WRITE_CNT
This reports the number of times anybody tried to write to a locked register. This is very useful to determine if the proper keys are being applied. If, after a program is run, this contains a non-zero value, the program is trying to write locked registers and is being denied.
Write 0x00 to reset.
0x11: GEN_TEST_WORD
This causes the current state of the config jumpers to be written to the REM_DATA_RD, for manufacturing test (but I suppose they could be used as general inputs if necessary.
Write any value to transfer the config jumper state once.
0x12: MOTOR_A_INVERT
0x13: MOTOR_B_INVERT
Motor inverts for the A and B channels. These are used on all boards, master and slave, to control the directions.
Writing 0x01 to either register causes the forward direction of that channel to be reversed
Writing 0x00 returns to the driver to default mode.
0x14: BRIDGE
This causes the channel B source mux to match channel A source in order to allow bridging.
Writing 0x01 to cause channel bridging.
Writing 0x00 to unbridge channels.
0x15: LOCAL_MASTER_LOCK
This register allows all other registers to be writeable, for unknown effect.
Write 0x9B to allow free register use.
Write other values to lock read-only registers.
0x16: LOCAL_USER_LOCK
This register allows the configuration registers to be locked from inadvertent access. Anything that can change modes is umbrelled by the user lock, but it is defaulted as unlocked. When locked, writing garbage data will invoke garbage motor movements but will not cause the configuration to be lost when correct data is returned. Any register with "USER LOCK" as "YES" can become read-only with this register. (Note: it is possible to accidently write the user lock key to this register with garbage data.)
Write 0x5C to prevent writes to configuration registers
Write other values to allow writes.
0x17: MST_E_IN_FN
This sets the behavior of the master SCMD's config_in line, on the expansion bus. The user can attach a wire to config_in, program this register, and send a pulse to cause the following behaviors:
0x00: Config_in has no effect
0x01: Full restart – The SCMD will reboot.
0x02: Re-enumerate slaves and resend 'slave configuration' – The enumeration state machines will be restarted. When complete, the master's local copy of intended slave behavior will be vended to the slaves. This may be useful in a situation where slaves are dropping and reappearing on the bus, and a full reconfiguration is not desired.

0x18: U_PORT_CLKDIV_U
0x19: U_PORT_CLKDIV_L
These registers report the clock dividers applied to the serial component's input clock. The CLKDIV_U register contains the upper 8 bits of a 16 bit word, while the CLKDIV_L contains the lower.
Writing has no effect.
0x1A: U_PORT_CLKDIV_CTRL
This register controls the associated clock divider registers. Write any value to cause the values in the U and L registers to be combined and applied to the clock component. The associated serial device will be re-initalized.
0x1B: E_PORT_CLKDIV_U
0x1C: E_PORT_CLKDIV_L
These registers report the clock dividers applied to the serial component's input clock. The CLKDIV_U register contains the upper 8 bits of a 16 bit word, while the CLKDIV_L contains the lower.
Writing has no effect.
0x1D: E_PORT_CLKDIV_CTRL
This register controls the associated clock divider registers. Write any value to cause the values in the U and L registers to be combined and applied to the clock component. The associated serial device will be re-initalized.
0x1E: U_BUS_UART_BAUD
This register reports the current UART baud rate, as indicated by a number. This is used internally by the master, and is read when UART reinitializaitons occur. Writing has no immediate effect but may cause the baud rate to change during other operations. The UART "U" command should be used to change baud, and not be done here.
Modes:
0x00: 2400
0x01: 4800
0x02: 9600
0x03: 14400
0x04: 19200
0x05: 38400
0x06: 57600
0x07: 115200

0x1F: PAGE_SELECT
This register is reserved for future PSoC based components that may need to access multiple pages of register data. It currently has no effect.
0x20: MA_DRIVE
0x21: MB_DRIVE
The output driver PWMs are directly controlled by these registers.
Writing a value from 0 to 255 sets the duty cycle of the associated channels on any board, master or slave. Note: Writing a value of 0x80 sets the duty cycle to 50%, which will appear as off at the outputs. Write values up and down from there for forward and backwards drive.
0x22: S1A_DRIVE through 0x41: S16B_DRIVE
These registers are used by the master to hold the slave drive information. Setting these registers sets the next value the master will send to the slave's MA_DRIVE and MB_DRIVE registers. See UPDATE_RATE and FORCE_UPDATE to control how often this information is pushed out to the slaves.
This register is unused in the slaves.
0x50: INV_2_9
0x51: INV_10_17
0x52: INV_18_25
0x53: INV_26_33
These registers set the inversion mode for all slave motors, as a bit pattern.
Writing data to this register causes the data to be instantlly transfered to the slaves. Setting a single bit in the register causes that motor number to be inverted.
When setting or clearing a single motor's inversion state, a read-modify-write operation should be done to maintain the existing configuration of other motors.
0x54: BRIDGE_SLV_L
0x55: BRIDGE_SLV_H
These registers set the bridging mode for all slave SCMDs, as a bit pattern.
Writing data to this register causes the data to be instantlly transfered to the slaves. Setting a single bit in the register causes that slave number to be bridged.
When setting or clearing a single driver's bridging state, a read-modify-write operation should be done to maintain the existing configuration of other motors.
0x70: DRIVER_ENABLE
This register controlls the driver enable line and can effectively remove all energy from the outputs.
Write 0x01: Enable this driver
Write 0x00: Disable this driver.
Writing data to this register as a master causes the master to send the configuration to the slaves. As a slave, writing data effects output drive only.
0x71: UPDATE_RATE
This register is used to determine how often to send data out to the slaves. The LSB is worth 1 ms, so the update rate can be set between 1 and 255 ms.
Write 0x00: Do not automatically update the slaves.
Write other values: Update at a rate of 1ms to 255 ms.
0x72: FORCE_UPDATE
When the UPDATE_RATE is set to 0x00, writing a non-zero value to this register causes the contents of the XXX_DRIVE registers to be send out to the slaves at the next available time (sent by enumeration state machines). This register is automatically cleared.
Write 0x01: Send the current drive values to the attached slaves
0x73: E_BUS_SPEED
Writing changes the expansion bus bitrate and re-initalizes the bus for the master, and has no effect for the slaves.
Available speeds:
0x00: 50kHz
0x01: 100kHz
0x02: 400kHz

0x74: MASTER_LOCK
This is a global lock location for the LOCAL_MASTER_LOCK.
Writing a value to this register causes the master to apply that value to it's own LOCAL_MASTER_LOCK, and transmit the value to all attached slave LOCAL_MASTER_LOCK registers.
0x75: USER_LOCK
This is a global lock location for the LOCAL_USER_LOCK.
Writing a value to this register causes the master to apply that value to it's own LOCAL_USER_LOCK, and transmit the value to all attached slave LOCAL_USER_LOCK registers.
0x76: FSAFE_TIME
This register sets the watchdog timeout time, from 10 ms to 2.55 seconds. The LSB is worth 10 ms.
Write 0x00: Do not use the watchdog.
Write other values: Set the watchdog timeout time to 10ms * value.
0x77: STATUS_1
This register uses bits to show status. Currently, only b0 is used.
Bit 0: Enumeration complete. Reads 1 if the master state machine has reached the fully enumerated state.
0x78: CONTROL_1
This register is unused.
0x79: REM_ADDR
Write the address of the slave to communicate with.
0x7A: REM_OFFSET
Write the register number to access of the slave.
0x7B: REM_DATA_WR
Write the data that will be written to the slave REM_OFFSET register, at the REM_ADDR.
0x7C: REM_DATA_RD
Read data from the slave REM_OFFSET register, at the REM_ADDR will be contained here.
0x7D: REM_WRITE
Write any value to initiate a remote write operation. The data in REM_DATA_WR will be written to the slave at REM_ADDR, at address REM_OFFSET. This register will be set to 0x00 automatically
0x7E: REM_READ
Write any value to initiate a remote read operation. The data in the slave at REM_ADDR, REM_OFFSET memory location will be copied to the REM_DATA_RD location, and this register will be automatically cleared.

# Program Architecture
The firmware is written to emulate a I2C or SPI perhiphreal. The register map is the core of the operation, and is surrounded by function calls that operate on the data. This allows the memory controller to report changed status of memory, and to record misuse of the memory.
During initialization, the SCMD:
- Clears and prepares the user space memory, setting default values and lock states
- reads the config jumpers
- Configures default hardware, isr and timer operation
- Initializes the PWM generators
- Calculates serial clock rates based on config jumpers
- Initializes its serial perhipheral blocks based on config jumpers
After the SCMD is initialized by the boot and initialization calls, it runs a loop that takes the following actions:
- Calls appropriated serial reception parser (or leave it up to the hardware ISRs to call)
- Steps the master or slave enumeration state machine
- Deals with changed register data
- Checks and deals with changes to hardware reset functions
The config jumpers change the general behavior and roll of the expansion port based on slave or master mode. Both rolls function the same regarding memory access and H-Bridge driver operation, but the master has more registers that are checked for changed values, and transmitts data to the slaves if necessary.
Illustration 3 shows how the master behaves. During master operation the user port directly controls the memory, and the master enumeration state machine is active. This state machine chooses how and when to deal with changing data and serves to look for slaves on the expansion bus.
Illustration 4 Shows how a slave behaves. The expansion bus then deals with the memory directly, and the slave enumeration state machine is active. It is a matching state machine to the master and waits to be discovered, then does things based on the data it has available.

Illustration 3: Topology of a SCMD in as a master (or single)
Illustration 4: Topology of a SCMD in as a slave
## Slave Address Enumeration
When the master is exploris the expansion bus, it assigns addresses to the attached slaves. This happens after a fresh power up, or by master config_in when MST_E_IN_FN is set to 0x02 for bus re-enumeration.
All slaves boot with the address 0x10 programmed into their I2C interfaces. 0x10 is reserved as an address that should never be accessed, it can have multiple devices with the same address at boot.
After a time delay, the master asserts the config_out line. Upon detection by the first slave, that slave switches address to 0x4A, the general poll address.
The master then polls 0x4A by looking for a valid ID word. When found, the master assigns an address to the slave at 0x4A. This causes that slave to assert their config_out line, readying the next slave. The master then assigns the next availble address and the cycle continues.
The operation is complete when the master fails 200 times to get an ID word, or if the programmed max slave address is reached. The SLV_TOP_ADDR is programmed with the address of the last slave in the chain as a way of counting how many slaves are present.
Illustration 5 shows actions taken by the master and slaves during enumeration. Arrows indicate direction of information flow within the system.

Illustration 5: Actions and communication of the expansion bus

### State diagrams
The master and slave state machines work together to accomplish I2C handshaking. These two diagrams impelemnt the handshaking outined in Illustration 5.

Illustration 6: The slave enumeration state machine

Illustration 7: The master enumeration state machine
### Boot timing
51515
### re-enumeration timing
## System Schematic
## File Descriptions