# index
Text

Serial Controlled Motor Driver Datasheet and Manual

# Features
Basic Features
- 127 levels of DC drive strength.
- Controllable by I2C, SPI, or TTL UART signals
- Stock 3.3v logic levels
- Direction inversion on a per motor basis
- Global Drive enable
- Expansion port utalizing I2C that allows 16 additional drivers
- Auto-enumeration of slaves based on connection of expansion 'In' and 'Out' connections.
- Exposed TO-220 heatsink shape
- 12 selectable I2C addresses

Advanced Features
- Bridging (between channels of a single board, to double current)
- VCC breakable to allow up to 5.5v levels.
- PSoC programming port included.
- Master can report bus diagnostics
- Configurable failsafe time and operation
- Configurable expansion bus bitrate to 50, 100, or 400 kHz.
- Configurable expansion bus update rate from 1ms to 255ms, or by command only.

Electrical and Thermal Specs
- 1.5 A peak drive per channel
- Operates from 3 to 11 volts with 12v absolute max
- Thermal limits
  - 500mA / channel -- T.case = 50 Deg C
  - 1A / channel -- T.case = 90 Deg C
  - 1.2A / channel -- T.case = 110 Deg C
  - 1.5A / channel -- forced air cooling or heatsink required
# Basic Ideas
Communication Perspective
A single driver board is capible of being expanded by adding one or more slaves. Illustration 1 shows a master connected to a slave, with the user controlling by microcontroller or computer.
Illustration 1: A basic topology

To avoid confusion, a few terms are defined here.
User Port – Connects the user’s project to the master SCMD and is unused on slaves.
Expansion Port – Connects a single master and up to 16 slaves, and should never be connected to the user’s project.
Master – The SCMD which is connected to the user’s project. Also, it is the I2C master on the expansion port
Slave – A SCMD which is only connected to a master scmd by way of the expansion port.
Note: The config in and out pins of the expansion port may sometimes be connected to the user’s project for error checking and mitigation purposes.

Motor Polarity – The driver and this document often omit motor polarity. This is because polarity to spin direction is not standardized, and it is assumed the user will attach them backwards 50% of the time. Each motor channel is independently configurable for what is thought of as ‘forward’ spin by command. It is assumed that the user will first attach the motors, then decide which channels need to be inverted and issue inversion settings at boot time.

Numbering – Each SCMD has two channels, A and B. When they are bridged the B channel becomes a duplicate A, and the drive is doubled.
Motors in a chain of several motor drivers are all referenced by motor number, starting from master's A channel as zero, B as 1, then the first slave's A channel as 2, and so on up to motor 33. When a driver board is bridged, it still has both motor numbers associated with it, however controlling what was the B channel will have no effect.

When performing bridging, driver board are numbered 0 to 16. The master is driver number 0, the first slave is driver 1, etc.
# Operational Description
Breif
The main elements of the motor driver are a microcontroller and dual H-bridge driver, with a voltage regulator for the logic end of things.

The SCMD has been designed to emulate a typical I2C or SPI perhipherial. Inside, there is a set of memory locations named registers. By writing into some registers, the SCMD takes action. Other registers have data that can be used, but writing does not cause action within the SCMD. Generally, the SCMD sits idle waiting for changes to registers, then performs actions based on new data.
During boot, the SCMD captures the contents of the config jumpers into a register and uses that value to determine which serial configuation to choose. They are set by entering a number from 0 to 15 in 4 bit binary, with a solder jumper indicating a '1'.
The SCMDs are equipted with an expansion I2C bus, wher they can be gained to form a group of motors that can all be controlled by talking to the master only.
For I2C busses, pull-up resistors are provided and default disabled. The slave bus requires a single set enabled for any number of slaves. If I2C is used, the user pull-up jumper must be closed, or pull-up resistors supplied externally.
The SCMD has been released with an Arduino library that performs high level functions by writing the correct registers, and can ease demonstration. The library also has functions to read or write the registers directly.
Register access aafeguards
Certain registers are designated "User unlockable". These registers contain configuration data for the current application. To provent accidental writes a user lock register exists. When the user lock contains the user key byte, the user lock registers can be written to. The default is unlocked.
Registers that are designated read-only are actually also writeable, to no documented end. A global lock exists to allow writes to these addresses. Note that the global lock is protected by the user lock, so both are needed to allow write access.
Slave operation
Multiple SCMDs can be connected to create a group of controllable motors. In this case, certain registers within the master cause changes to the slaves.
Writing to the drive registers in the master do not instanly update the drive levels. Instead, the master saves the new drive levels and sends them to the slaves on a periodic loop (configurable rate or by manual request). There are 34 registers that contain drive levels for each of the possible motor numbers. Writing to any of these registers in the master causes that motor in the slave chain to match the drive level after the next transmission.
Writing to the "Global setting" registers cause immediate action. The register contents will be applied locally and then sent out to the slaves.
H-Bridge driver control
The H-Bridge driver is essentially a dual, two leg totem pole drive with control logic. The default power-on state is to have the drives completely disabled with all 4 outputs at zero. Configuring the SCMD causes the driver to connect to two PWM generators, choosing polarity and source. They can be configured such that both outputs will be time and duty syncronized, allowing bridging of the output terminals for double current.
Power-on enumeration
When power is first applied, the master operates at the selected serial confiuration and address, and all slaves exist on an address that is not used. When the master is ready, it triggers the first driver to move to a polling address, and accept an assigned address from there. In turn, each slave receives an address in this manner.
When the master can't get a response within a set number of tries, enumeration stops and the master is ready to accept control.
Failsafe operation
The default operation of the SCMD is to simply drive the motors at the last level indicated until another command come in. To pervent run-away situations a Failsafe is implemented. When configured, the drivers will remove power to the outputs if the serial bus remains inactive for a period of time, which can be set up to 2.5 seconds.
The config in pin on the master and slaves can also work as a reset line. For the slaves, bringing the line low. resets the device. For the master, pulsing the line can cause either low-level reboot or re-enumeration of the slaves.
Using these two features, a system can be made to recover from many situations.
Status LED
There is a single LED on the motor driver, that blinks to indicate status, and blips to indicate serial port activity. A normally operating blinks once with much space inbetween while an error state will be displayed as a fast group of flashing. Reception of data will cause a slight blip in the LED. When a steady stream of data is being received, the LED will display dim with the other status message overlaid.
# Electrical properties
## Absolute maximum
## Electrical Characteristics
## Thermal
# Pin functions

# Communication interfaces
## User port I2C
## User port SPI

## User Port UART and Command Set
General:
All commands delimited by \n.
If command length exceeds buffer, bus will return "ovf" (overflow). Send delimiter to clear buffer
If command not valid, bus will return "inv" (invalid syntax)
If command not formatted correctly, bus will return "fmt" (formatting error)
If command addresses motor on slave which is not present, bus will return "nom" (no motor)

Drive motor:
"Mndl"
n = motor number, single or double digits
d = direction, R or F
l = level, 0 to 100

Example:
"M1F34" – Drive master motor B forward at 34%.
"M2R80" – Drive slave motor A reverse at 80%.

Switch motor polarity:
"MnS"
n = motor number, single or double digits

Example:
"M1S" – Switch polarity of motor 1. F becomes R, and vicea-versa.

Write register:
"Wrrhh"
rr = two digit hex address
hh = two digit hex data

Example:
"W20FF" – Write 0xFF to register 0x20 (MA_DRIVE).

Read register:
"Rrr"
rr = two digit hex address

Example:
"R01" – Read address 0x01 (ID), bus will display "A9", ID word of 0xA9

UART Baud:
"Un"
n = baud rate selection

Rates supported:
1 – 2400
2 – 4800
3 – 9600
4 – 14400
5 – 19200
6 – 38400
7 – 57600
8 – 115200

Example:
"U3" – Set baud rate to 9600
"U8" – Set baud rate to 115200

Bridge/unbridge outputs:
"Brr"
rr = Motor driver number, 0 is master, 1-16 is slave

Example:
"B0" – Bridge master's outputs
"B2" – Bridge the 2nd physical slave's outputs (motors 4&5)

Enable/disable outputs:
"E"

Example:
"E" – Enable all outputs
"E" (a second time) – Disable all outputs
## Expansion port
# Control registers

## Memory map

## Descriptions
# Arduino Library API Reference
moar text

## Slave Address Enumeration
The master is capible of exploring the expansion bus and assigning addresses to the attached slaves. This happens after a fresh power up, or by master config_in when MST_E_IN_FN is set to 0x02 for bus re-enumeration.
All slaves boot with the address 0x10 programmed into their I2C interfaces. 0x10 is reserved as an address that should never be accessed, it can have multiple devices with the same address at boot.
After a time delay, the master asserts the config_out line. Upon detection by the first slave, that slave switches address to 0x4A, the general poll address.
The master then polls 0x4A by looking for a valid ID word. When found, the master assigns an address to the slave at 0x4A. This causes that slave to assert their config_out line, readying the next slave. The master then assigns the next availble address and the cycle continues.
The operation is complete when the master fails 200 times to get an ID word, or if the programmed max slave address is reached. The SLV_TOP_ADDR is programmed with the address of the last slave in the chain as a way of counting how many slaves are present.
d
# Program Architecture
In
order

d
### State diagrams

The other diagram

### Boot timing
51515
### re-enumeration timing
## Program Flowchart

## System Schematic
## File Descriptions