# [Title page]
# index
text
# Features
som text
# Application diagram
# Electrical properties
## Absolute maximum
## Nominal
## Thermal
# Pin functions
# Communication interfaces
## User port I2C
## User port SPI
## User Port UART and Command Set
General:
All commands delimited by \n.
If command length exceeds buffer, bus will return "ovf" (overflow). Send delimiter to clear buffer
If command not valid, bus will return "inv" (invalid syntax)
If command not formatted correctly, bus will return "fmt" (formatting error)
If command addresses motor on slave which is not present, bus will return "nom" (no motor)

Drive motor:
"Mndl"
n = motor number, single or double digits
d = direction, R or F
l = level, 0 to 100

Example:
"M1F34" – Drive master motor B forward at 34%.
"M2R80" – Drive slave motor A reverse at 80%.

Switch motor polarity:
"MnS"
n = motor number, single or double digits

Example:
"M1S" – Switch polarity of motor 1. F becomes R, and vicea-versa.

Write register:
"Wrrhh"
rr = two digit hex address
hh = two digit hex data

Example:
"W20FF" – Write 0xFF to register 0x20 (MA_DRIVE).

Read register:
"Rrr"
rr = two digit hex address

Example:
"R01" – Read address 0x01 (ID), bus will display "A9", ID word of 0xA9

UART Baud:
"Un"
n = baud rate selection

Rates supported:
1 – 2400
2 – 4800
3 – 9600
4 – 14400
5 – 19200
6 – 38400
7 – 57600
8 – 115200

Example:
"U3" – Set baud rate to 9600
"U8" – Set baud rate to 115200

Bridge/unbridge outputs:
"Brr"
rr = Motor driver number, 0 is master, 1-16 is slave

Example:
"B0" – Bridge master's outputs
"B2" – Bridge the 2nd physical slave's outputs (motors 4&5)

Enable/disable outputs:
"E"

Example:
"E" – Enable all outputs
"E" (a second time) – Disable all outputs
## Expansion port
# Control registers
## Memory map

## Descriptions
# Arduino Library API Reference
moar text
# Program Architecture
In order
## Slave Address Enumeration
The master is capible of exploring the expansion bus and assigning addresses to the attached slaves. This happens after a fresh power up, or by master config_in when MST_E_IN_FN is set to 0x02 for bus re-enumeration.
All slaves boot with the address 0x10 programmed into their I2C interfaces. 0x10 is reserved as an address that should never be accessed, it can have multiple devices with the same address at boot.
After a time delay, the master asserts the config_out line. Upon detection by the first slave, that slave switches address to 0x4A, the general poll address.
The master then polls 0x4A by looking for a valid ID word. When found, the master assigns an address to the slave at 0x4A. This causes that slave to assert their config_out line, readying the next slave. The master then assigns the next availble address and the cycle continues.
The operation is complete when the master fails 200 times to get an ID word, or if the programmed max slave address is reached. The SLV_TOP_ADDR is programmed with the address of the last slave in the chain as a way of counting how many slaves are present.

### State diagrams

### Boot timing
51515
### re-enumeration timing
## Program Flowchart

## System Schematic
## File Descriptions