# [Title page]
# index
Text
## Nomenclature
There are a few terms with specific meanings. When User and Expansion are used, it referring to the physical pins of the connection. When Master and Slave are used it matches the I2C behavior on the expansion port, and refers to the connected chain of SCMDs.

User Port – Connects the user’s project to the master SCMD and is unused on slaves.
Expansion Port – Connects a single master and up to 16 slaves, and should never be connected to the user’s project.
Master – The SCMD which is connected to the user’s project. Also, it is the I2C master on the expansion port
Slave – A SCMD which is only connected to a master scmd by way of the expansion port.

Note: The config in and out pins of the expansion port may sometimes be connected to the user’s project for error checking and mitigation purposes.

Motor Polarity – The driver and this document often omit motor polarity. This is because polarity to spin direction is not standardized, and it is assumed the user will attach them backwards 50% of the time. Each motor channel is independently configurable for what is thought of as ‘forward’ spin by command. It is assumed that the user will first attach the motors, then decide which channels need to be inverted and issue inversion settings at boot time.

Expansion Bus I2C Pull-Ups – The default pull-up state of the expansion bus is disabled. This is because pull-up resistors should be applied thoughtfully and not just whenever the designer is unsure. A side effect is that a single master’s expansion bus is shipped in an invalid state, and will cause the driver to detect an error. A single master without slaves should have its Exp. PU jumper closed.

Motor Numbering – The SCMD’s silkscreen shows connections for motor ‘A’ and motor ‘B’. This is purposefully not numeric to prevent confusion within a programming environment.

Many library functions ask for a ‘motor number’ to tell the library which particular motor to address in the chain. For addressing’s sake, the motor attached to the master at position ‘A’ will always be motor 0, and the ‘B’ position, motor 1. The first slave device attached will have motors 2, and 3, at positions ‘A’ and ‘B’ respectively. Slave 2 will have motors 4, and 5, and so on.

When a SCMD is designated as bridged mode, it loses whatever motor is attached to the ‘B’ position, and any information sent to control the ‘A’ position will control both outputs synchronously, such as inversion or drive strength.

Example: In a configuration with 1 master and 2 slaves, with the first slave being bridged, motor positions 0 and 1 drive the master’s ‘A’ and ‘B’ channels, position 2 drives the first slave’s bridged motor, positions 4 and 5 drive the second slave’s ‘A’ and ‘B’ channels, and position 3 has no effect.
# Features
som text
# Application diagram
# Electrical properties
## Absolute maximum
## Electrical Characteristics
## Thermal
# Pin functions
# Communication interfaces
## User port I2C
## User port SPI
## User Port UART and Command Set
General:
All commands delimited by \n.
If command length exceeds buffer, bus will return "ovf" (overflow). Send delimiter to clear buffer
If command not valid, bus will return "inv" (invalid syntax)
If command not formatted correctly, bus will return "fmt" (formatting error)
If command addresses motor on slave which is not present, bus will return "nom" (no motor)

Drive motor:
"Mndl"
n = motor number, single or double digits
d = direction, R or F
l = level, 0 to 100

Example:
"M1F34" – Drive master motor B forward at 34%.
"M2R80" – Drive slave motor A reverse at 80%.

Switch motor polarity:
"MnS"
n = motor number, single or double digits

Example:
"M1S" – Switch polarity of motor 1. F becomes R, and vicea-versa.

Write register:
"Wrrhh"
rr = two digit hex address
hh = two digit hex data

Example:
"W20FF" – Write 0xFF to register 0x20 (MA_DRIVE).

Read register:
"Rrr"
rr = two digit hex address

Example:
"R01" – Read address 0x01 (ID), bus will display "A9", ID word of 0xA9

UART Baud:
"Un"
n = baud rate selection

Rates supported:
1 – 2400
2 – 4800
3 – 9600
4 – 14400
5 – 19200
6 – 38400
7 – 57600
8 – 115200

Example:
"U3" – Set baud rate to 9600
"U8" – Set baud rate to 115200

Bridge/unbridge outputs:
"Brr"
rr = Motor driver number, 0 is master, 1-16 is slave

Example:
"B0" – Bridge master's outputs
"B2" – Bridge the 2nd physical slave's outputs (motors 4&5)

Enable/disable outputs:
"E"

Example:
"E" – Enable all outputs
"E" (a second time) – Disable all outputs
## Expansion port
# Control registers
## Memory map

## Descriptions
# Arduino Library API Reference
moar text
# Program Architecture
In order
## Slave Address Enumeration
The master is capible of exploring the expansion bus and assigning addresses to the attached slaves. This happens after a fresh power up, or by master config_in when MST_E_IN_FN is set to 0x02 for bus re-enumeration.
All slaves boot with the address 0x10 programmed into their I2C interfaces. 0x10 is reserved as an address that should never be accessed, it can have multiple devices with the same address at boot.
After a time delay, the master asserts the config_out line. Upon detection by the first slave, that slave switches address to 0x4A, the general poll address.
The master then polls 0x4A by looking for a valid ID word. When found, the master assigns an address to the slave at 0x4A. This causes that slave to assert their config_out line, readying the next slave. The master then assigns the next availble address and the cycle continues.
The operation is complete when the master fails 200 times to get an ID word, or if the programmed max slave address is reached. The SLV_TOP_ADDR is programmed with the address of the last slave in the chain as a way of counting how many slaves are present.

### State diagrams

### Boot timing
51515
### re-enumeration timing
## Program Flowchart

## System Schematic
## File Descriptions