# Buses
## Test the I2C user interface
This test checks all the ways a user can connect the I2C interface.

Procedure:
1. Test the following configurations:
  1. SCMD master at any lowest address, 100 kHz redboard
  2. Two SCMD masters, one at highest address, 100 KHz redboard
  3. 400 KHz on teensy (Low priority)
2. For each configuration, run the diag example and look for errors.

Criteria:
Did the EUTs behave normally?? YES/NO

## Test the SPI user interface
This test checks all the ways a user can connect the SPI interface.

Procedure:
1. Test the following configurations:
  1. SCMD master at 1 MHz
  2. Two SCMD masters with different CS pins.
2. For each configuration, run the diag example and look for errors.

Criteria:
Did the EUTs behave normally? YES/NO

## Test the UART user interface
Procedure:
1. Test the following configurations:
  1. SCMD at default baud
  2. SCMD at 57600 baud by jumper
  3. SCMD at 115200 baud by jumper
  4. Other configurations by using the commands U0-U7.
2. Test that the number are accepted as 1 or two digit for most, and 3 for drive percent
3. Test that E, B, and MxxS commands result in the proper bit flipped within INV_X_X, BRIDGE_SLV_X and ENABLE registers

Criteria:
Did the EUTs behave normally?? YES/NO
# FW elements
For these tests, connect 16 slaves and perform the following actions using the registerRWtool
## Test motor driving registers
Make sure motor information is passed to the correct locations

Procedure:
1. Test that the following motors drive when master locations are written:
  1. motor 1, 2, 10, 17, 18, 25, 26, and 33

Criteria:
Do commands cause correct change on all motors? YES/NO

## Test slave configuration
Test that writing to slave and global registers passes the information on to the slaves correctly. For these tests remote access is required by remote window or arduino function. Inspected slave locations are 0x50, 0x53, 0x54, 0x57, 0x58, 0x5B, 0x5C and 0x5F.

Procedure:
1. Write a pattern to INV regs and read remote local inversion regs.
2. Write a pattern to BRIDGE regs and read remote local bridging regs
3. Check that the following are passed directly (global config) to the associated local slave registers.
  1. DRIVER_ENABLE
  2. MASTER_LOCK
  3. USER_LOCK
  4. FSAFE_TIME

Criteria:
Are all values passed correctly? YES/NO

## Test enumeration
Check that enumeration occurs correctly. For many of these, reading 0x0B for top address may be useful.

Procedure:
1. Check that enumeration occurs successfully for 1, 2, and 16 slaves.
2. Issue a reboot by CONTROL_1 for 16
3. Configure some global settings
4. Issue a re-enumeration by CONTROL_1 for 16 slaves
5. Check that global settings were correctly passed to slaves
6. Configure master config in pin with MST_E_IN_FN and test function by shorting config_in to ground

Criteria:
1. Does the top address match for various slaves? YES/NO?
2. Do both reboots result in a proper enumeration? YES/NO?
3. Do both reenumerations result in the correct configuration? YES/NO?
## Test the expansion bus speed setting
Check that the expansion bus can be configured by inspecting with a scope.

Procedure:
1. Measure the bit rate of the defualt 100KHz setting
2. Configure and test the 50KHz and 400 KHz settings using E_BUS_SPEED
3. Measure the slave motor data packets dead time, and set UPDATE_RATE to change
4. With UPDATE_RATE set to 0, does a packet occur after writing FORCE_UPDATE to 1?

Criteria:
Are bus configuration parameters effecting operation properly? YES/NO

## Check lock protections
Make sure the master and user locks operate

Procedure:
1. Write each "R" register with master key removed, then use REG_OOR_CNT to verify if they were protected
2. Write each "user lock"able register with the user key removed, then use REG_OOR_CNT to verify they did not accept the data.
3. Write each "user lock"able register with the user key inserted, REG_OOR_CNT should read 0.
4. Write a new FID in with both keys inserted, and read back to verify.

Criteria:
Were the locks capible of preventing or allowing the correct operations? YES/NO

## Test the failsafe mode
This checks that all modes of failsafe operate

Procedure:
1. Probe config out and exp. data
2. Set the FSAFE_TIME(0x76) to 0xC8 for 2 second failsafe time
3. Set FSAFE_CTRL:
  1. Use b1 for drive off/last behavior
  2. Set 0x02 for reboot
  3. Set 0x04 for re-enumerate.
  4. Set 0x08 for user port re-init.
  5. Set 0x10 for expansion port re-init
4. Check the slave contents of FSAFE_TIME to determine if configuration was properly transfered during re-enumerate.

Criteria:
Did the EUT recover as expected? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO

## Test an item in the Test Plan
Describe the intent of the itme to be tested

Procedure:
1. First step to testing
2. Second step to testing

Criteria:
Describe acceptable test results as a question? YES/NO