# index
Text
# Serial Controlled Motor Driver Datasheet and Programming

# Features
Basic Features
- 127 levels of DC drive strength.
- Controllable by I2C, SPI, or TTL UART signals
- Stock 3.3v logic levels
- Direction inversion on a per motor basis
- Global Drive enable
- Expansion port utalizing I2C that allows 16 additional drivers
- Auto-enumeration of slaves based on connection of expansion 'In' and 'Out' connections.
- Exposed TO-220 heatsink shape
- 12 selectable I2C addresses

Advanced Features
- Bridging (between channels of a single board, to double current)
- VCC breakable to allow up to 5.5v levels.
- PSoC programming port included.
- Master can report bus diagnostics
- Configurable failsafe time and operation
- Configurable expansion bus bitrate to 50, 100, or 400 kHz.
- Configurable expansion bus update rate from 1ms to 255ms, or by command only.

Electrical and Thermal Specs
- 1.5 A peak drive per channel
- Operates from 3 to 11 volts with 12v absolute max
- Thermal limits
  - 500mA / channel -- T.case = 50 Deg C
  - 1A / channel -- T.case = 90 Deg C
  - 1.2A / channel -- T.case = 110 Deg C
  - 1.5A / channel -- forced air cooling or heatsink required
## Basic Ideas
Common Terms
This document talks about relationships between multiple boards in the sames system. To avoid confusion, a few terms are defined here.
User Port – Connects the user’s project to the master SCMD and is unused on slaves.
Expansion Port – Connects a single master and up to 16 slaves, and should never be connected to the user’s project.
Master – The SCMD which is connected to the user’s project. Also, it is the I2C master on the expansion port
Slave – A SCMD which is only connected to a master scmd by way of the expansion port.
Note: The config in and out pins of the expansion port may sometimes be connected to the user’s project for error checking and mitigation purposes.

Motor Polarity – The driver and this document often omit motor polarity. This is because polarity to spin direction is not standardized, and it is assumed the user will attach them backwards 50% of the time. Each motor channel is independently configurable for what is thought of as ‘forward’ spin by command. It is assumed that the user will first attach the motors, then decide which channels need to be inverted and issue inversion settings at boot time.

Motor Numbering – The SCMD’s silkscreen shows connections for motor ‘A’ and motor ‘B’. This is purposefully not numeric to prevent confusion within a programming environment.

Many library functions ask for a ‘motor number’ to tell the library which particular motor to address in the chain. For addressing’s sake, the motor attached to the master at position ‘A’ will always be motor 0, and the ‘B’ position, motor 1. The first slave device attached will have motors 2, and 3, at positions ‘A’ and ‘B’ respectively. Slave 2 will have motors 4, and 5, and so on.

When a SCMD is designated as bridged mode, it loses whatever motor is attached to the ‘B’ position, and any information sent to control the ‘A’ position will control both outputs synchronously, such as inversion or drive strength.

Example: In a configuration with 1 master and 2 slaves, with the first slave being bridged, motor positions 0 and 1 drive the master’s ‘A’ and ‘B’ channels, position 2 drives the first slave’s bridged motor, positions 4 and 5 drive the second slave’s ‘A’ and ‘B’ channels, and position 3 has no effect.
# Operational Description
General Description
The main elements of the motor driver are a microcontroller and dual H-bridge driver, with a voltage regulator for the logic end of things.

The User port is designated for connection to the user’s project (which will tell the motors what to do), and can be configured as UART, SPI, or I2C by jumper setting.
The Expansion port is configured as I2C master or slave based on jumper settings, and operates on a second I2C bus with only other motor drivers.
The microcontroller generates PWM signals that go straight to the DRV8835 motor driver, which consists of 2 mosfet H-bridge driver circuits with thermal and current protection built in.
The SCMD has been designed to emulate a typical I2C or SPI perhipherial. Inside, there is a set of memory locations called registers. By writing into some registers, the SCMD takes action. Other registers have data that can be used, but writing does not cause action within the SCMD. Generally, the SCMD sits idle waiting for changes to registers, then performs actions based on new data.
The SCMD has been released with an Arduino library that performs high level functions by writing the correct registers, and can ease demonstration. It is acceptable to use the library or write the registers directly.
Operating with slaves.
Multiple SCMDs can be connected to create a group of controllable motors. In this case, certain registers within the master cause changes to the slaves.

Writing to the drive registers in the master do not instanly update the drive levels. Instead, the master updates local drive levels and sends data to the slaves on a periodic loop (configurable rate or by manual request). There is a register specified for each motor that can exist in the chain. Writing to any of these registers in the master causes that motor in the slave chain to match the drive level.
Writing to the "Global setting" registers cause immediate action. The register contents will be applied locally and then sent out to the slaves.
H-Bridge driver control
The H-Bridge driver is essentially a dual, two leg totem pole drive with control logic. The default power-on state is to have the drives completely disabled with all 4 outputs at zero. Configuring the SCMD causes the driver to connect to two PWM generators, choosing polarity and source. They can be configured such that both outputs will be time and duty syncronized, allowing bridging of the output terminals for double current.
Power-on enumeration
When power is first applied, the master operates at the selected serial confiuration and address, and all slaves exist on an address that is not used. When the master is ready, it triggers the first driver to move to a polling address, and accept an assigned address from there. In turn, each slave receives an address in this manner.
When the master can't get a response within a set number of tries, enumeration stops and the master is ready to accept control.
# Electrical properties
## Absolute maximum
## Electrical Characteristics
## Thermal
# Pin functions

# Communication interfaces
## User port I2C
## User port SPI
## User Port UART and Command Set
General:
All commands delimited by \n.
If command length exceeds buffer, bus will return "ovf" (overflow). Send delimiter to clear buffer
If command not valid, bus will return "inv" (invalid syntax)
If command not formatted correctly, bus will return "fmt" (formatting error)
If command addresses motor on slave which is not present, bus will return "nom" (no motor)

Drive motor:
"Mndl"
n = motor number, single or double digits
d = direction, R or F
l = level, 0 to 100

Example:
"M1F34" – Drive master motor B forward at 34%.
"M2R80" – Drive slave motor A reverse at 80%.

Switch motor polarity:
"MnS"
n = motor number, single or double digits

Example:
"M1S" – Switch polarity of motor 1. F becomes R, and vicea-versa.

Write register:
"Wrrhh"
rr = two digit hex address
hh = two digit hex data

Example:
"W20FF" – Write 0xFF to register 0x20 (MA_DRIVE).

Read register:
"Rrr"
rr = two digit hex address

Example:
"R01" – Read address 0x01 (ID), bus will display "A9", ID word of 0xA9

UART Baud:
"Un"
n = baud rate selection

Rates supported:
1 – 2400
2 – 4800
3 – 9600
4 – 14400
5 – 19200
6 – 38400
7 – 57600
8 – 115200

Example:
"U3" – Set baud rate to 9600
"U8" – Set baud rate to 115200

Bridge/unbridge outputs:
"Brr"
rr = Motor driver number, 0 is master, 1-16 is slave

Example:
"B0" – Bridge master's outputs
"B2" – Bridge the 2nd physical slave's outputs (motors 4&5)

Enable/disable outputs:
"E"

Example:
"E" – Enable all outputs
"E" (a second time) – Disable all outputs
## Expansion port
# Control registers
## Memory map

## Descriptions
# Arduino Library API Reference
moar text
# Program Architecture
In order
## Slave Address Enumeration
The master is capible of exploring the expansion bus and assigning addresses to the attached slaves. This happens after a fresh power up, or by master config_in when MST_E_IN_FN is set to 0x02 for bus re-enumeration.
All slaves boot with the address 0x10 programmed into their I2C interfaces. 0x10 is reserved as an address that should never be accessed, it can have multiple devices with the same address at boot.
After a time delay, the master asserts the config_out line. Upon detection by the first slave, that slave switches address to 0x4A, the general poll address.
The master then polls 0x4A by looking for a valid ID word. When found, the master assigns an address to the slave at 0x4A. This causes that slave to assert their config_out line, readying the next slave. The master then assigns the next availble address and the cycle continues.
The operation is complete when the master fails 200 times to get an ID word, or if the programmed max slave address is reached. The SLV_TOP_ADDR is programmed with the address of the last slave in the chain as a way of counting how many slaves are present.

### State diagrams

### Boot timing
51515
### re-enumeration timing
## Program Flowchart

## System Schematic
## File Descriptions